## Slide 1: Memory consumption reduction in onu adapter.
Channel sizes in FSMs.
Mib template instances.
The go channel sizes in FSMs in onu-adapter were defaulted to size of 2048, which is not required. This was consuming lot of memory as the FSMs will be initialized for each ONU and each one would have separate 2048 channel. This is now reduced to size 2.

## Slide 2: MIB template, existing implementation
MIB Template 1
MIB instance per ONUs
In the existing implementation, a MIB template is generated for each model+swversion of an ONU.
Each ONU coming up with that model_swVersion will have a MIB instance along with ONU specific data generated .
If there are 2k ONTs of the same type then 2k instances will be generated, which is not necessary.
This would consume quite a bit of memory for each ONU, which is nothing but a copy of the same MEs but with only different MAC and serialnumber different.
MIB instance per ONUs
MIB instance per ONUs
MIB instance per ONUs

## Slide 3: MIB template, new implemenation
MIB Template 1
With the new implementation, the MIB instance will be only one maintained per type.
This will reduce the number of instances, for the same type only 1 instance will be used.
Of course the ONU specific data will still be kept separate per ONU.
This will reduce the memory consumption PER ONU.
One MIB instance per MIB template